## 1.	Identification of the Substance and company

1.1

| Other names: | Iron ore pellets, pellets, nodules, briquettes, pellet fines, pellet chips | REACH Registration No.: | xx-xxxxxxxxxx-xx-xxxx |
| --- | --- | --- | --- |
| EINECS no.: | 265-996-3 | CAS no.: | 65996-65-8 |

1.2

Iron ore pellets are composed essentially of di-iron trioxide, Fe2O3  >90% with toxicologically insignificant amounts of amounts of gangue constituents comprised of the silicates and oxides of calcium, silicon, magnesium and aluminium. The product of agglomerating iron ore fines, concentrates and other iron-bearing materials at 1100 to 1300°C. Iron ore pellets are used as a feedstock in blast furnaces and also in other forms of iron production. Pellet fines or chips are the product of screening pellets prior to shipment and are typically used as feedstock for production of iron sinter.

Uses: SU14; PC7, PC19; PROC 2,8b, 14, 22, 26; ERC1 (see section 16 for detailed descriptions)

1.3

| Company: | Split cells to add more than one company address |
| --- | --- |
| Telephone: | Split cells to add more than one company telephone number |
| Normal Hours: | Split cells to add more than one company contact |
| Email: | Split cells to add more than one company email address |

1.4

| Emergency: | Split cells to add more than one company emergency contact |
| --- | --- |

## 2. 	Hazards Identification

2.1

Iron ores, agglomerates are inert solids and do not meet the requirements for classification as dangerous under both the EU Dangerous Substances (67/548/EEC) Directive and secondly according to the Classification, Labelling and Packaging of substances and mixtures (CLP) regulations (EC 1272/2008).

The principal risk to human health presented by iron ore agglomerates is dust relating to the concentration of dust in the air acting as a poorly soluble inert nuisance dust. The higher the concentration of dust the greater the risk of irritation to the respiratory system and mechanical irritation to the eyes. Iron oxide pellets may contain respirable crystalline silica (RCS). Experience along with testing shows that in practice no values of RCS content in iron ore agglomerates are found above 0.1%. Concentrations above 1.0% trigger a classification as STOT RE 2 for the silicosis hazard. Therefore this does not trigger a classification for this substance.

2.2

No label required, no signal word required.

2.3

There are no further hazards for the substance iron ore agglomerates.

## 3.	Composition / information on ingredients

3.1

Iron ores, agglomerate composition is usually expressed in terms of its bulk composition the typical range is shown in the table below.  It is conventional to represent the bulk composition of oxide materials, such as minerals, ores and refractory products, in terms of the simple oxides of the constituent elements.  However, this does not imply that the product is composed of such simple compounds it is simply a convenient means of representing the overall composition of the material. See table below.

| Substance | Range (%) by weight | Classification (Dangerous Sub DIr) | Classification (CLP Regs) |
| --- | --- | --- | --- |
| Fe2O3 | >80.0 | Not classified | Not classified |
| Fe | 60.0-69.0 | Not classified | Not classified |
| SiO2 | <10.0 | Not classified | Not classified |
| CaO | <8.0 | Not present as CaO so not classified | Not present as CaO so not classified |
| MgO | <5.0 | Not classified | Not classified |
| Al2O3 | <3.0 | Not classified | Not classified |
| P | <0.2 | Not classified | Not classified |
| S | <0.1 | Not classified | Not classified |
| Free moisture at 105°C | 0-6.0 | Not classified | Not classified |

## 4. 	First aid measures

4.1

Skin contact:	None required, just maintain good level of hygiene by washing.

Eye contact:	Irritation.  Wash the eye with running water for at least ten minutes. Seek medical advice if irritation persists.

Inhalation:	Physical irritation.  Remove to fresh air.

Ingestion:	None required.

4.2

For eye exposure soreness and irritation are the main symptoms.  For inhalation coughing is the main symptom.  Remove the exposed operator to an area away from high dust levels.

4.3

Not applicable for this substance.

## 5. 	Fire fighting measures

Iron ores, agglomerates is non-flammable and has a high melting point of >1000°C.

5.1

Not flammable so not applicable for this substance.

5.2

Not flammable so not applicable for this substance.

5.3

Not flammable so not applicable for this substance.

## 6. 	Accidental release measures

Contain and collect any spillage of this solid and return to the suitable storage facility.  If the solid is dry and dusty wetting should be used to reduce wind entrainment of dust particles.

## 7. 	Handling and Storage

7.1 	Handling

Use automated mechanical equipment to handle iron ores, agglomerates so that personal contact is minimised.  Minimise generation of dust by using mechanical shovels and equipment instead of handheld tools.  Ideally vacuum suction systems / extraction systems should be used to remove dust when cleaning areas of plant. If the environment is dusty then suitable and approved respiratory protection should be worn (see section 8).

7.2	Storage

Generally stored in stockpiles in open air during dry conditions the iron ores, agglomerates may need to be kept damp through water spraying to minimise dust release through wind entrainment.  Use of surfactants, wetting agents, etc. are another method of dust suppression.  Fixed sided buildings or barriers could also be erected to prevent release of dust.  At the blast furnace covered bunkers are the most effective method of storage.

## 8. 	Exposure controls and personal protection

8.1	Control parameters (Occupational Exposure Limits (OELs))

Current OELs (GESTIS International Limit Values Institut fuer Arbeitsschutz der Deutschen Gesetzlichen Unfallversicherung (IFA))

| Country in EU with OEL for the relevant substance | Substance |
| --- | --- |
|  | Iron oxide (Fe2O3 & FeO) | Dust inhalable | Dust respirable |
|  | 8 hr TWA (mg/m3) | STEL (mg/m3) | 8 hr TWA (mg/m3) | STEL (mg/m3) | 8 hr TWA (mg/m3) | STEL (mg/m3) |
| Austria | 5.0 (resp) | 10.0 (resp) | 10.0 | 20.0 | 5.0 | 10.0 |
| Belgium | 5.0 | --- | 10.0 | --- | 3.0 | --- |
| Denmark | 3.5 | 7.0 | 10.0 | 20.0 | --- | --- |
| France | --- | --- | 10.0 |  | 5.0 | --- |
| Germany (AGS) | --- | --- | 10.0 | 20.0 | 3.0 | 6.0 |
| Germany (DFG) | --- | --- | 4.0 | --- | 1.5 | --- |
| Hungary | 6.0 (resp) | --- | 10.0 | --- | 6.0 | --- |
| Poland | 5.0 | 10.0 | --- | --- | --- | --- |
| Spain | 5.0 | --- | 10.0 | --- | 3.0 | --- |
| Sweden | 3.5 | --- | 10.0 | --- | 5.0 | --- |
| United Kingdom | 5.0 | --- | 10.0 | --- | 4.0 | --- |
| TWA - Time Weighted Average measured over an 8 hour period |
| STEL - Short Term Exposure Limit Value – 15 minute duration |
| Resp - Respirable fraction of dust |

8.2	Control Measures

Automated systems are recommended to minimise the risk of exposure by avoiding the need for the presence of operators under normal circumstances. The use of mechanical equipment such as vacuum systems or other extraction methods should take precedence over manual work. For large amounts of built up dust the use of machinery, such as a small mobile mechanical shovel units could be used to collect and transport dust to a skip.  The use of water suppression should be considered in conjunction with the use of mechanical methods so as to reduce the risk of dust disturbance.

If it is not feasible to use vacuum methods or machinery, then the manual use of shovels should be considered as a last resort to remove settled dust.  If there is a risk of disturbing dust and creating high airborne dust concentrations then, as a last resort, the wearing of suitable and approved respiratory protective equipment should be implemented.  Ori-nasal respirators fitted with a P3 filter (EN149 : FFP3S) may be used when dust levels are high, the manufacturer’s directions for use must be followed at all times to achieve the correct and proper face fit.

Eye protection such as safety glasses / goggles of an approved standard could be used to prevent dust contact with the eyes.

From an environmental perspective, the storage and handling of iron ores, agglomerates can give rise to releases of dust as drift. Airborne dusts may originate from stockpiles and conveyor belts. Dust suppression techniques include the orientation of materials in the direction of the prevailing winds and the use of water sprinkler systems.

## 9.	Physical and chemical properties

| Property | Value used |
| --- | --- |
| Physical State at 20°C/ 1013 hPa | Solid |
| Melting point | >1000 °C at 1013 hPa |
| Boiling point | Not applicable, iron ore agglomerates have a melting point of >300°C |
| Relative density | 5.0 g/cm3 at 20°C |
| Vapour pressure | Not applicable for iron ore agglomerates due to high melting point >1000°C |
| Surface tension | Not applicable, iron ore agglomerates are inorganic solids with very low aqueous solubility |
| Water solubility | 0.05 µg/L at 25 °C, the aqueous solubility of iron ore agglomerates is so low that it does not become bioavailable to humans or ecosystems |
| Partition coefficient (Kow4) | Not applicable, inorganic |
| Flash point | Not applicable, iron ore agglomerates are inorganic solids with a melting point >1000°C |
| Flammability | Non flammable |
| Explosive properties | Non explosive |
| Oxidising properties | No |
| Granulometry | Iron ore agglomerates are produced as a hard agglomerate consisting of spheres of diameter > 8 mm. The substance as used therefore does not contain particles in the inhalable size range. Pellet size is 5.0-20.0mm, Pellet fines size is <10.0mm |
| Stability in organic solvents | Stable in organic solvents |
| Dissociation constant | Insoluble |
| Viscosity | Solid |

## 10.	Stability and reactivity

Iron ores, agglomerates are stable and do not react violently or dangerously with other substances under normal conditions.

## 11.	Toxicological information

The main route of exposure to iron ores, agglomerates is via inhalation of the dust which may be produced through abrasion, although oral exposure could also occur. Iron ores, agglomerates are inert solids and not toxic. The principal risk to human health presented by iron ores, agglomerates dust is related to the concentration of dust in the air acting as a nuisance dust. The higher the concentration of dust the greater the risk of irritation to the respiratory system and mechanical irritation to the eyes.

##### Acute toxicity

Iron oxides are practically insoluble in water and, hence, they will not pass through the skin. The aqueous layer of the skin is not acidic enough to give rise to the formation of iron ions. It has been demonstrated that even at rather low pH levels, the solubility is very low. Without the chemical conversion into soluble iron ions, systemic exposure will be negligible, and toxicologically insignificant.

Certain studies have typically shown that after exposure to iron oxide via inhalation, a recruitment of pulmonary macrophages in the lungs was observed, indicating the activation of the main mechanism for pulmonary clearance of such insoluble particles. Fe2O3 particles were observed to be phagocytosed by these macrophages. Such elevations tend to decrease rapidly and usually reach control levels some days post-exposure. According to the authors of several of these studies, the effects are first and foremost non-specific reversible responses to an increased dust burden in the lung, clearly associated with the ‘particle effect’. Beck et al. (1982) state ‘we do not think the increases seen after exposure to iron oxide in our system are precursors of chronic pulmonary damage, based on both published data on hamsters (Zaidi, 1969) and on our preliminary histopathological examination of lung tissue from exposed hamsters’.

No classification is required for acute toxicity for oral, dermal and inhalation exposure with values of LD50 (oral): 10,000 mg/kg bw and LC50 (inhalation): 2100 mg/m³ air recorded which are far beyond any classification setting.

##### Skin corrosion / irritation

As iron oxides are practically insoluble in the aqueous layer on the skin, exposure to iron ions will be negligible, which means that irritating effects of dissolved iron can be ruled out. Iron ores, agglomerates along with other iron oxides typically behave as poorly soluble particles and can be seen as not irritating or not corrosive to the skin.

##### Eye damage / irritation

If any damage to the eye occurs, this would most likely be due to mechanical damage, and thus, not related to the chemical composition of the substance itself. For instance, potential occupational exposure of the eye to this substance is very common in manual work.  Iron ores, agglomerates along with other iron oxides typically behave as poorly soluble particles and can be seen as not chemically irritating or not chemically corrosive to the eyes. Irritation or damage can only occur by mechanical means.

##### Respiratory  / Skin sensitisation

Iron ores, agglomerates along with other iron oxides typically behave as poorly soluble particles and can be seen as not sensitising to the respiratory system or the skin. Skin contact with rust, which can contain several kinds of iron oxides, has been very common since time immemorial in everyday life of humans. However, skin sensitisation owing to dermal contact with rust has not been reported in literature as a recognised problem. Moreover, as iron oxides are practically insoluble in the aqueous layer of the skin, exposure to iron ions will be negligible, which means that skin sensitisation by dissolved iron can be ruled out.

##### Germ cell mutagenicity

Owing to the lack of solubility of iron oxides, genetic toxicity is not expected, unless the particles are phagocytosed by the cells. This can be ruled out in the case of bacterial assays (Ames test), since phagocytosis does not occur. Regarding the mammalian cell mutagenicity, Fe3O4 particles were indeed observed within the cell in the chromosome aberration test but still, no mutagenic response was exerted. The aforementioned result can also be expected when other iron oxide particles are tested. Particle size is a determinative factor; large iron oxide particles, produced by abrasive techniques, will not enter the mammalian cell and thus iron ores, agglomerates should not be seen as a mutagenic substance.

##### Carcinogenicity

The assessment of cancer risk due to pure exposure to iron oxides alone is difficult, since most industrial activities which may give rise to iron oxide exposure generate mixed exposures containing several different chemicals and dusts, or radiation.  While excess risks of lung cancers have been reported in epidemiological studies of iron ore miners, foundry workers, steel workers and welders, industrial settings where exposure to iron oxides were involved, the majority of the studies were not able (or did not intend) to separate iron oxide exposure from other exposures to known or suspected carcinogens often present at the same settings or same workplaces.

Four epidemiological studies of good quality have been conducted, which either tried to separate iron oxide exposure from other exposures (Moulin et al. 2000 and Bourgkard et al. 2009 in the iron and steel industry) or which have been conducted under circumstances in which only low levels of exposure to other agents were present (Axelson et al. 1979 among workers exposed to iron oxide during production of sulphuric acid from pyrite and Lawler et al. 1985 among iron-ore miners).  These studies, specifically addressing the affect of iron oxide on lung cancer, did not show any risk of lung cancer associated with exposure to iron oxides.

Institutions like IARC (1987) or ACGIH (2006) have reviewed the available information regarding the carcinogenicity of iron oxides and found iron oxides not to be a carcinogen.

##### Reproductive toxicity

No evidence of any effects. Human exposure to iron oxides occurs via skin contact with large solid objects, or via the inhalation or ingestion (primary or secondary) of small particles (dusts). Based on the physico-chemical properties of iron oxides, any significant systemic exposure upon skin contact can be deemed unlikely. With respect to the oral and inhalation (particles are ingested after clearance from the respiratory tract) route, after ingestion (primary or secondary), the oxides will not be dissolved in the gastric juice due to their physicochemical properties; they will be efficiently eliminated as such via the faeces. Therefore, systemic exposure will not occur to any significant extent.

##### Repeated dose toxicity - Inhalation

Results of inhalation studies clearly show the iron oxide particles to behave as poorly soluble particles. This together with the lack of bioavailability after oral exposure and dermal exposure signifies that no classification for repeated-dose toxicity is necessary.

However repeated high exposures to iron oxide over long periods of time could possibly cause a benign pneumoconiosis known as siderosis.  This condition is not thought to cause any impairment of lung morphology, functions or symptoms.  Therefore the conditions occurring after the prolonged inhalation high levels of iron or iron compounds as placed on the market do not meet the criteria for classification as dangerous under CLP (Iron Platform Position paper TWG65 - Siderosis Position Paper100125).

## 12.	Ecological information

12.1	Toxicity

Iron in massive form and sparingly soluble forms of iron are highly insoluble and non-hazardous. Literary studies have extensively used test solutions with iron concentrations above that of its solubility limit. Due to the physical effects of precipitated material some of these studies are meaningless for the investigation of intrinsic toxicity. Iron ions released to surface waters quickly form insoluble iron hydroxides in mixing zones. These positively charged iron (III) colloids will react with the negatively charged mucus that lines the fish gill. This accumulation of iron on fish gills results in physical effects. In ambient conditions, dissolved natural background concentrations of iron, are generally at equilibrium therefore an addition of iron would lead to the precipitation of iron compounds from solution and are therefore not intrinsically toxic (Jackson, Versfeld & Adams 2010,Peters, Brown & Merrington 2010).

Iron is amongst the most common elements in the earth’s crust and can be found in great abundance in both the terrestrial and sediment environment. The relative contributions of anthropogenic iron to the existing natural pools of iron in soils and sediments is therefore not relevant, neither in terms of added amounts, nor in terms of toxicity (Vangheluwe, Vercaigne, Vandenbroele, Heijerick & Shtiza 2010).

Avian toxicity data are used in the assessment of secondary poisoning risks for the aquatic and terrestrial food chains where iron is an essential trace element, well regulated in all living organisms. Differences in iron uptake rates are related to essential needs, varying with the species, size, life stage, seasons etc. Iron homeostatic mechanisms are applicable across species with specific processes being active depending on the species, life stages, etc. The available evidence shows the absence of iron bio-magnification across the tropic chain both in the aquatic and terrestrial food chains. The existing information suggests not only that iron does not biomagnify, but rather that it tends to exhibit biodilution. Differences in sensitivity among species are not related to the level in the trophic chain, but to the capability of internal homeostasis and detoxification (Vangheluwe and Nederkassel 2010).

12.2	Persistence and Degradability

Iron ores, agglomerates are highly insoluble, so in general (abiotic) degradation is an irrelevant process for inorganic substances that are assessed on an elemental basis.

12.3	Bioaccumulative potential

Iron is an essential trace element, well regulated in all living organisms. The available evidence shows the absence of iron biomagnification across the trophic chain, both in the aquatic and terrestrial food chains. The existing information suggests not only that iron does not biomagnify, but rather that it tends to exhibit biodilution (Jackson, Versfeld, Adams 2010 & Vangheluwe & Nederkassel 2010).

12.4	Mobility in soil

Iron in massive form and iron oxides are highly insoluble and non-hazardous and therefore demonstrate that the aqueous solubility of iron ores, agglomerates is so low that it does not become bioavailable to ecosystems and will not show mobility in the soil.

12.5	Results of PBT and vPvB assessment

Iron ores, agglomerates are not bio-available, owing to extreme insolubility in water, are not systemically available or bio-accumulative and hence do not fulfil either of the PBT and vPvB criteria for classification.

## 13.	Disposal considerations

Iron ores, agglomerates should always be recycled.  If iron ore agglomerates are not fed into a blast furnace or other similar iron / steel making systems they should be recycled back into the process by either the producer or by another company.

## 14.	Transport information

Iron ore agglomerates are not classified as dangerous under CLP or Dangerous Substances Directive for transport so there is no requirement for transport information. All subheadings in this section are not applicable for iron ores, agglomerates.

## 15.	Regulatory information

15.1

Iron ores, agglomerates are not covered by any other local or national legislation in relation to their intrinsic properties, but differences at national level may apply and this should be taken into account.  The process of iron ore pellet production including its emissions is covered by the European Commission document “Integrated Pollution Prevention and Control Reference Document on Best Available Techniques for the Iron and Steel Production Draft 2001” (Iron and Steel BREF current standard 2001).  This safety data sheet does not cover these types of emission and the BREF document should be used in this case. Occupational exposure limits (OELs) set by each member state and are covered by their own policy and legislation where this exists. There are no Authorisations and Restrictions on use under REACH for the substance iron ores, agglomerates.

15.2

A Chemical Safety Assessment has not been carried out as iron ores, agglomerates do not meet the requirements for being classified as dangerous.

## 16.	Other Information

##### Revision

This safety data sheet has been produced / revised in line with Annex II of the REACH Regulations (2010).  Information in this safety data sheet was collected and used where necessary from the work done to produce a REACH Registration dossier and Chemical Safety Report for iron ores, agglomerates. This revision is the current version dated December 2010

Previous Versions: Month - year

Abbreviations  / Acronyms of significance

| ERC1 | Manufacture of substances |
| --- | --- |
| LD50 | Median lethal dose, causing 50% lethality |
| LC50 | Median lethal concentration, causing 50% lethality |
| PC7 | Base metals and alloys |
| PC19 | Intermediate |
| PROC 2 | Use in closed process, no likelihood of exposure - Continuous process but where the design philosophy is not specifically aimed at minimizing emissions. It is not high integrity and occasional expose will arise e.g. through maintenance, sampling and equipment break-ins |
| PROC8b | Transfer of substance or preparation (charging/discharging) from/to vessels/large containers at dedicated facilities |
| PROC14 | Production of preparations or articles by tabletting, compression, extrusion, pelettisation |
| PROC22 | Potentially closed operations with minerals/metals at elevated temperature - Activities at smelters, furnaces, refineries, coke ovens. Exposure related to dust / fumes to be expected. Emission of direct cooling may be relevant |
| PROC26 | Handling of solid inorganic substances at ambient temperature - Transfer / handling of ores, concentrates, raw metal oxides and scrap; packaging, un-packaging, mixing/blending, weighing of metal powders and other minerals |
| SU14 | Manufacture of basic metals |

Risk and Safety Phrases according to (67/548/EEC):

Iron ores, agglomerates are not classified as dangerous and do not have any R and S phrases assigned.

Hazard and Precautionary Statements according to CLP Regulations (EC)1272/2008):

Iron ores, agglomerates are not classified as dangerous and do not have any H and P statements assigned.

References

ACGIH (2006). Iron oxide. ACGIH. Documentation of the threshold limit values and biological exposure indices Vol:7th Ed (2006).

Axelson O, Sjoberg A. (1979). Cancer incidence and exposure to iron oxide dust. J Occup Med 21(6):419-422.

Beck BD, Brain JD, and Bohannon DE. (1982). An in vivo hamster bioassay to assess the toxicity of particulates for the lungs. Toxicology and Applied Pharmacology, 66: 9-29.

Bourgkard E, Wild P, Courcot B, Diss M, Ettlinger J, Goutet P, Hemon D, Marquis N, Mur JM, Rigal C, Rohn-Janssens MP, Moulin JJ. (2009). Lung cancer mortality and iron oxide exposure in a French steel-producing factory. Occup Environ Med 66 (3):175-81.

DFG (1984). Eisenoxid. Deutsche Forschunsgemeinschaft: toxikologisch-arbeitsmedizinische Begruendung von MAK-Werten.

European Commission document “Integrated Pollution Prevention and Control Reference Document on Best Available Techniques for the Iron and Steel Production Draft April 2010” (Iron and Steel BREF current version 2001)

GESTIS International Limit Values Institut fuer Arbeitsschutz der Deutschen Gesetzlichen Unfallversicherung (IFA) – website: http://bgia-online.hvbg.de/LIMITVALUE/WebForm_gw.aspx

IARC (1987a). Haematite & iron oxide. IARC Monographs An Updating of IARC Monographs Volumes 1 to 42. Supplement 7 p.216.

IARC (1987b). Iron & steel founding. IARC Monographs. An Updating of IARC Monographs Volumes 1 to 42. Supplement 7 p.224.

Iron Platform Technical Working Group (2010b). Does the occurrence of siderosis or pulmonary fibrosis after prolonged exposure of workers to iron or iron compounds require these substances to be classified as causing specific target organ toxicity (STOT) under CLP? TWG65 - Siderosis Position Paper100125, Owner company: The Iron Platform.

Jackson K., Versfeld R., Adams W. (Iron Platform). 2010. Position Paper – Predicted No Effect Concentration. Iron Platform, UK.

Lawler AB, Mandel JS, Schuman LM, Lubin JH (1985). A retrospective cohort mortality study of iron ore (hematite) miners in Minnesota. J Occup Med 27(7):507-517.

Moulin JJ, Clavel T, Roy D, Dananche B, Marquis N, Fevotte J, Fontana JM. (2000). Risk of lung cancer in workers producing stainless steel and metallic alloys. Int Arch Occup Environ Health 73(3):171-180.

Peters A., Brown B., Merrington G. 2010. Background Paper on Iron in the Aquatic Environment. WCA Environment, UK.

Vangheluwe M. & Nederkassel J. van (Arche). 2010. White Paper on waiving for secondary poisoning for Fe and Al compounds – Final report. ARCHE, Belgium.

Vangheluwe M., Vercaigne I., Vandenbroele M., Heijerick D. (ARCHE) & Shtiza A. (ARCADIS). 2010. White Paper on exposure based waiving for iron and aluminium in soil and sediments - Final report. ARCHE, Belgium.

Disclaimer

The information, specifications, procedures, and recommendations herein are presented in good faith and are believed to be accurate and reliable at the date of issue.  Where information is taken from supplied items it is the responsibility of the supplier to ensure the accuracy of the data.  The Individual authors of this safety sheet are deemed to be appropriately competent.  This safety data sheet template was constructed under the requirements of the REACH regulations ((EC) No 1907/2006) using the guidance provided as to the format and information necessary.  Occupational exposure limits (OEL) used in this safety data sheet template will be EU OELs and where these limits do not exist appropriate member state OELs will be the reference limit.  No liability can be accepted with regard to the handling, processing or use of the product concerned which, in all cases, shall be in accordance with appropriate regulations and or legislation.  Company name gives no warranty or representation as to the accuracy of the information or for the guidance being for, or suitable for, a specific purpose.  All implied warranties and conditions are excluded, to the maximum extent permitted by law. Use of this document by any third party is at your own risk. Save to the extent that liability cannot be excluded by law, Company name is in no way responsible or liable for any damage or loss whatsoever arising from the use of or reliance on the information and guidance contained in this document.